## Slide 1: ARP Packet Format
Destination address
Source address
Type
0x8060
ARP or RARP
Padding
CRC
Hardware type - 2bytes
Protocol type - 2bytes
Operation code - 2bytes
Hardware address length - 1byte
Protocol address length - 1byte
Source hardware address
6
6
2
28
10
Ethernet header
Source protocal address
Target protocal address
Target hardware address
4

## Slide 2: ARP Flow
192.168.0.100
11:11:11:11:11:11
192.168.0.200
22:22:22:22:22:22
ARP Request (Broadcast)
ARP Reply (Unicast)
Source hardware address – 11:11:11:11:11:11
Source protocol address – 192.168.0.100
Destination hardware address – 00:00:00:00:00:00
Destination protocol address – 192.168.0.200
Source hardware address – 22:22:22:22:22:22
Source protocol address – 192.168.0.200
Destination hardware address – 11:11:11:11:11:11
Destination protocol address –192.168.0.100